| Instruction to candidates |
| --- |
| Before starting each practical task Candidates must: discuss the task with the tutor before starting check the vehicle / training rig is appropriate and in a satisfactory condition for the task wear the correct PPE (personnel protective equipment) obtain the correct vehicle details and data complete a Health & Safety and risk assessment and complete the section on the record sheet complete the vehicle details and data section on the record sheet before commencing the task (to be checked by tutor / assessor) obtain the necessary tools and equipment check the tools and equipment to make sure they are in a safe working condition document / report any faulty tools (not use them if they are unsafe) answer the questions in each of the sections complete the self assessment section when the task has been completed Skills integration: Numeracy skills Each task incorporates numeracy skills including: addition, subtraction, multiplication and division. Candidates will be using many different types of measuring equipment; these are used to measure parts of a millimetre up to complete metres. Other measurements will be taken when carrying out compression and pressure testing, cylinder leakage and exhaust emission tests. There are also some calculations involving electrical units. By using these practical task sheets, numeracy skills can be integrated and supported into the core curriculum. Communication skills During these tasks there will be the opportunity for: group discussion with regard to Health & Safety within the workshop environment taking instructions and being provided with support from instructors and tutors completing task worksheets and feeding back on problems found during the task presentation skills within the written work using wall charts and vehicle manuals for information. ICT skills Vehicle information is often accessed via computer using systems such as AUTODATA. Many of the diagnostic tools used for the modern vehicle involves the use of computer diagnostics. Word processing the task sheets will help improve ICT skills. |  | During each practical task Candidates must: use tools and equipment safely at all times document all relevant readings report any breakages show their tutor relevant stages of the task, as requested (ie component removal) refit all nut /bolt /washers/fixings complete all parts of the task answer all questions relating to the task and complete the self assessment section return all tools and equipment in a safe and clean condition Tutors/assessors must: check vehicle details and data feedback on performance sign off and date completed task Problem solving All tasks involve having to work things out and identifying vehicle system faults (engine, chassis, transmission, ancillary electrical), this will provide opportunities for problem solving. Working with others Many of the tasks involve working with others to lift, push, pull, and hold vehicle units and components. Effective communication is an important aspect of vehicle work in order to maintain a safe working environment. Improving own learning Every task will provide an opportunity to improve learning. In most cases Candidates would not have carried out these tasks before and therefore distance travelled can easily be measured. A series of practical assessments will need to be carried out; this will determine the practical skills and competences gained. Environmental issues Education for sustainable development and global citizenship – ESDGC (Wales only) Each task involves using power, energy and materials, some of which can be recycled and some which need to be disposed of. These can be identified and Candidates will need to state how this was carried out and the possible effects on the environment. |

| Task tracking document |
| --- |
| Tasks | Date completed | Comments on Candidate’s own performance (not signed by the tutor/assessor) |
| 1. Workshop investigation |  |  |
| 2. Safe lifting of a vehicle using a trolley jack |  |  |
| 3 Use of tyre fitting equipment |  |  |
| 4. Wheel and tyre balancing |  |  |
| 5. Change oil and filter |  |  |
| 6. Changing brake pads |  |  |
| 7. Removal and refitting of a front suspension unit |  |  |
| 8. Removal and refitting of brake drums and shoes |  |  |
| 9. Remove and test a thermostat, check antifreeze. Make gasket and refit thermostat |  |  |
| 10. Remove, check and replace Serpentine – Poly V drive belt & check alternator charging |  |  |
| 11. Under bonnet level checks & air filter |  |  |
| 12. Fit a number plate to a vehicle |  |  |
| 13. Soldering exercise |  |  |
| 14. Block and stud manufacture |  |  |
| 15. Spark plug and HT lead checks |  |  |
| 16. Remove and replace a clutch unit |  |  |
| 17. Pop riveting task |  |  |
| 18. Using a multimeter to test components |  |  |
| 19. Remove and replace track rod ends and check alignment |  |  |
| 20. Remove and replace exhaust silencer and check emission readings |  |  |
| 21. Remove and replace a cylinder head gasket using the correct tightening procedures |  |  |
| 22. Remove and refit headlamp unit and check alignment |  |  |
| 23. Cam belt change on a CI (diesel) engine |  |  |
| 24. Remove and replace a suspension strut (Macpherson type). Remove and replace spring |  |  |
| 25. Brake light switch removal, test and refit |  |  |
| 26. Using an engine fault code reader |  |  |
| 27. Repair puncture in tyre |  |  |

Workshop investigation                                                                                  Job number 1

| Vehicle workshop investigation Carry out a vehicle workshop investigation to identify the main areas where you will be working in. You need to identify the following: main working area, tool stores, fire extinguishers, fuel store, exit points, hand wash area, vehicle lifts, first aid kit, pillar drill, bench grinder, battery store and any other important significant areas. Draw a plan of the workshop and show the position of the items listed above. You will need to use a PENCIL AND RULER not ink. Candidate’s name: |
| --- |
|  | Feedback from assessor: Signature: Date: ____/_____/______ |

Safe Lifting of Vehicle using a trolley jack                                                          Job number 2

| Safe lifting of a vehicle using a trolley jack Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (communication/numeracy skills) Make/Model of vehicle:_______________________________________________ Engine capacity:_____________________________________________________ Approximate vehicle weight:____________________________________________ SWL of lifting equipment:______________________________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:______________________________ Where is the trolley jack to be positioned:____________________________ Where are the support stands to be positioned:___________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. Support stands:_______________________________________ Trolley jack:_______________________________________ Other as necessary:__________________________________ | Questions to answer: (problem solving / improving own learning) How many support stands are used:___________________________ What would you do with a trolley jack which leaked oil: _________________________ What do the letters SWL stand for: ______________________________________ State two places the jack or support stands must not be placed under: 1.______________________________________________________________ 2.______________________________________________________________ 3.______________________________________________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly: ____________________________ Was the environment effected by your work:_______________________ Tools returned and stored correctly:__________________________ |
| Work results: self assessment for practical skills Workarea left tidy and tools stored correctly:_________________________ Vehicle lifted safely with correct positioning of lift and stands:____________ State if any damage was caused while carrying out this task:_____________ | Feedback from assessor Signature Date ____/_____/______ |

Use of tyre fitting equipment                                                                Job number 3

| Use of tyre fitting equipment Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:_________________________________________________ Engine capacity:_______________________________________________________ Recommended vehicle tyre size and pressure:______________/_______________ Wheel nut torque:___________________________ Nm |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn: __________________________ Eye/ ear/ head protection needed (state): _______________________ Other risks identified:_______________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tyre fitting hand tools:__________________/ Vehicle lift:___________ Tyre fitting machine make:_______________________________ Tyre fitting lubricant:__________/ Torque wrench:____________ Air line and pressure gauge:_____________________________ | Questions to answer: (problem solving / improving own learning) What is the minimum legal tread depth: _____________________mm What is the purpose of tyre fitting lubricant:_________________________________ How should the torque wrench be left after use:_____________________________ What is the technical name for a tyre pressure valve:_________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:_______________________ All tools returned and stored correctly:____________________ |
| Work results: self assessment for practical skills Work area left tidy and tools stored correctly:____________________________ Tyre fitted without damage:_________________________________ Tyre pressure setting:________________________ Wheel nuts/bolts fitted and correctly tightened:________________________ Vehicle left clean and tidy:_________________________________________ | Feedback from assessor Signature Date___/_____/_______ |

Wheel and tyre balancing                                                                            Job number 4

| Wheel and tyre balancing Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:_________________________________________________ Engine capacity:_______________________________________________________ Wheel nut torque:______________________________________ Type of wheels being balanced (steel/alloy/wire):____________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:_______________________________________ Type of balance machine:_______________________________________ Torque wrench:________________________________________________ All tools returned and stored correctly:_______________________________ | Questions to answer: (problem solving / improving own learning) How many wheel nuts/bolts per wheel:_____________________________ Total value of balance weights used:____________________________________ In what position, on the wheel rim, did you place the weights:__________________ _________________________________________________________________ What would the driver experience with an out of balance wheel:__________________ Are the balance weights self adhesive on or knock on: _________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All area left tidy and tools stored correctly:_________________________ |
| Work results: self assessment for practical skills Wheel fitted correctly:___________________________________________ Balance machine final reading:____________________________________ All nuts/bolts fitted and correctly tightened:___________________________ | Feedback from assessor Signature Date ___/_____/____ |

Change oil and filter	                                                                            Job number 5

| Change oil and filter Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:_________________________________________________ Engine capacity:_______________________________________________________ Oil capacity:_____________ Make and type of oil:_________________________ Tightening method for oil filter:__________________________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:_______________________________________ Oil drain:___________________________________________ Torque wrench:______________________________________ Oil filter strap/wrench/chain/tool:_________________________ | Questions to answer: (problem solving / improving own learning) What marks are on the dip stick:___________________________________ What colour is the vehicle oil warning light :_________________________ State two checks to make after changing the oil and filter: 1._____________________________________ 2._____________________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:_______________________ All tools returned and stored correctly:_____________________ |
| Work results: self assessment for practical skills Work area left tidy and tools stored correctly:______________________ Filter removed and fitted:_____________________________________ Drain plug fitted and tightened with torque wrench:__________________ Drain plug sealed and oil level correct:_____________________________ Engine runs without leaks:_______________________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Changing brake pads                                                                            Job number 6

| Changing brake pads Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:________________________ Wheel nut torque:_________ Nm Minimum disc thickness:________ mm: Minimum brake pad thickness:_________ mm Minimum disc run–out:___________ mm Brake fluid normal boiling point:_________________________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:_________________________________________ DTI and Micrometer:_____________________________________ Ruler:________________________________________________ Brake fluid tester:_______________________________________ All tools returned and stored correctly:_____________________ | Questions to answer: (problem solving / improving own learning) State the number of pistons in the brake calliper:_______________ Why do some vehicles use a ventilated disc:___________________________ Has the vehicle got anti lock brakes (ABS):____________________________ What brake fluid is normally used:_______________________________________ What are the purpose of the wires attached to the brake pads:____________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:_______________________ All area left tidy and tools stored correctly:_________________________ |
| Work results: self assessment for practical skills Brake pads removed and refitted correctly:_____________________________ Thickness of brake pad material left:______________________________________ mm Disc run-out reading and disc thickness:__________ mm: __________mm Brake fluid test result:___________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Removal and refitting of a front suspension unit                                                                         Job number 7

| Removal of and refiiting of a front suspension unit Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:____________________ Wheel nut torque:____________ Nm Suspension mounting bolt torques:__________________________________ Nm |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn: _________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ Ball joint splitter if applicable:_______________________ Torque wrench:_______________________ | Questions to answer: (problem solving / improving own learning) How would you check a suspension damper:_______________________________ State a symptom of a broken suspension spring:_____________________________ List any faults found on the front suspension: ___________________________________________________________________ ___________________________________________________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills Front suspension unit fitted correctly:_____________________________ Any faults in the unit reported to assessor:_________________________ Type of spring fitted to unit:_____________________________________ All nuts/bolts fitted and correctly tightened:___________________________ | Feedback from assessor Signature Date ____/_____/____ |

Removal and refitting of brake drums and shoes                                                             Job number 8

| Removal and refitting of brake drums and shoes Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle: _______________________________ Minimum brake shoe wear: ________ mm: Maximum drum run-out:__________ mm State the expected hand brake limit:______________________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn: _________________________________ Eye/ ear/ head protection needed (state): _______________________________ Other risks identified:_________________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ DTI:_______________________ Ruler:_______________________ Torque wrench:__________________________ | Questions to answer: (problem solving / improving own learning) Name the two shoes fitted inside the drum: 1._________________ 2. _____________ How many operating cylinders are fitted inside the drum assembly: _______________ State a symptom if fluid was leaking onto the brake shoes:______________________________ Are the brakes manual or self adjusting type: _________________________________ Faults identified:_________________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:_________________________________ Was all waste disposed of correctly:________________________________ Was the environment effected by your work:_________________________________ All tools returned and stored correctly:_________________________________ |
| Work results: self assessment for practical skills Brake shoes removed and refitted:_______________________ Readings for drum ovality and wear:____________________ mm / ___________ mm Condition of brake shoes and lining thickness:______________________________ All nuts/bolts fitted and correctly tightened:_________________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Remove and test a thermostat, check antifreeze.  Make gasket and refit thermostat                                           Job number 9

| Remove and test a thermostat, check antifreeze. Make gasket and refit thermostat Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:______________________________________________ Engine normal running pressure and temperature:____________ / ____________ Antifreeze frost protection:__________________ and percentage:_______________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ Coolant boiling equipment:______________________ Thermometer:______________________ Pressure and Antifreeze tester:______________________ | Questions to answer: (problem solving / improving own learning) What is the thermostat gasket made from: State a symptom of lack of antifreeze in the coolant: Which component in the cooling system maintains the correct pressure: What drives the water pump: Name two materials which are used to make a radiator: 1. __________ 2. _________ Faults identified:_______________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:_______________________________ Was all waste disposed of correctly:_______________________________ Was the environment effected by your work:_______________________________ Was the environment effected by your work:_______________________________ All tools returned and stored correctly:_______________________________ |
| Work results: self assessment for practical skills Thermostat removed and fitted:__________________/gasket made:____________ State antifreeze frost protection:__________________ State any coolant leaks after pressure testing:_____________________________ All nuts/bolts fitted correctly and area left clean:____________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Remove, check and replace Serpentine – Poly V drive belt & check alternator charging                               Job number 10

| Remove, check and replace Serpentine – Poly V drive belt & check alternator charging Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle _________________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ Multi-meter (Volts DC):________________________ | Questions to answer: (problem solving / improving own learning) State two things that would happen if the belt failed: 1. ____________________________________________________________ 2. ____________________________________________________________ What is the approximate length of the serpentine belt:_________________ mm What should happen to the battery voltage when the engine is running above normal idle speed:________________________________________________________ Faults identified:_______________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills State the condition the of belt:_____________________________________________ Battery voltage engine not running:_________________________ Volts Battery voltage engine running above normal idle speed:_______ Volts Belt refitted correctly and all nuts/bolts fitted:_____________________ | Feedback from assessor Signature Date ____/_____/_______ |

Under bonnet level checks/air filter	                                                                Job number 11

| Under bonnet vehicle level checks & air filter Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:__________________ Engine capacity:_________________ Oil type: _______ Brake fluid type:_______ Power steering fluid if applicable:______ Air filter change interval:_____ Antifreeze change interval:___ Brake fluid:_______ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________________________ Battery hydrometer / refract meter:______________________ Brake fluid temperature test equipment:__________________ Antifreeze Test equipment:____________________________ | Questions to answer: (problem solving / improving own learning) What would happen if the air filter element was left out:_______________________ _____________________________________________________________________ What happens to brake fluid over time:______________________________________ At what intervals should the owner of a vehicle carry out level checks:______________________ Faults identified:_______________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills Condition of the air filter:__________________________________________ All levels checked and topped up: (oil, coolant, brake fluid, power steer, brake fluid) __________________________________________________________________ Hoses checked for serviceability:______________________________________ Work area left clean and tidy:___________________________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Fit a number plate to a vehicle                                                          Job number 12

| Fit a number plate to a vehicle (measuring exercise) Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:__________________ Front or rear number plate to be fitted:___________________________ Type of fixings to be used:____________________________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ Drill:______________________ Ruler:_______________________ | Questions to answer: (problem solving / improving own learning) What is the legal size for number plate letters:_______________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills Number plate fitted in correct position and level:______________________ Fixings correct and number plate secure:______________________ Work area left clean and tidy:______________________________________ Vehicle left clean and tidy:____________________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Soldering exercise	              Job number 13

| Soldering exercise Complete the, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | (Communication/Numeracy skills) Task planning 100mm Solder joint Two lengths of wire, 100mm, solder to make a ‘T’ shape and solder a terminal to either end. Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ Soldering iron:______________________ Solder/flux/wire/terminals:____________________________________________ |  |
| Work results: self assessment for practical skills Wire cut to length:______________________________ mm Terminals correctly and neatly soldered:_________________________________ Wrap joint correctly soldered:_____________________________________ Working area left clean and tidy:_________________________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Block and stud manufacture                                                  Job number 14

| Block and stud manufacture Complete the Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | (Communication/Numeracy skills) 25mm 75mm 75mm 6mm 8mm Manufacture a block 25mm x 25mm x 75mm. Produce two threads in the block, one a blind hole, the other all the way through. These should be drilled to accept 6mm and 8mm threads. Manufacture two studs which will fit these threads; both 75 mm in length. Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools are checked before use, used correctly and returned in good condition. General tools:______________________ Drill and bits:______________________ Taps/Dies:_________________________ Measuring equipment:__________________________ |  |
| Work results: self assessment for practical skills Block and studs manufactured to tolerance:__________________________ Threads allow smooth operation:___________________________________ Presentation and finish acceptable:_________________________________ Working area left clean and tidy:________________________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Spark plugs and HT leads checks                                         Job number 15

| Spark plugs and HT lead checks Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:__________________ Engine firing order:_______________ Spark plug gaps:__________________ mm Spark plug tighten torque:_________ Nm Spark plug (HT) lead resistance should be approximately 15-25KOhm/meter |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ Multi-meter/ohms:______________________ Feeler blades/ torque wrench:_________________________ | Questions to answer: (problem solving / improving own learning) Are the plug leads serviceable:_________________________________ Which part of the plug do you adjust to provide the correct the gap:________________ What will be the effect if the plug leads are fitted to the wrong plugs:_____________________ Faults identified:_______________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills Spark plug gaps adjusted to:________________________________ Plug leads fitted in the correct order:__________________________ Plug leads resistances: 1._________ 2._________ 3.__________ 4.__________ Plug lead lengths: 1.________ 2._________ 3.__________ 4.___________ Engine runs smoothly:________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Remove and replace a clutch unit	              Job number 16

| Remove and replace a clutch unit Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:__________________ FWD/RWD: State type: ____________ Clutch pressure plate torque:____________ Nm Method of clutch operation (hydraulic- mechanical - air):______________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ Clutch alignment tools:______________________ Torque wrench:____________________________ Engine/transmission support:_________________ | Questions to answer: (problem solving / improving own learning) State a symptom of oil on the clutch ilinings:_____________________________________ State the correct order when tightening clutch cover bolts:____________________ What component does the clutch centre plate drive:______________________________ Is there a provision for clutch adjustment:_________________ Faults identified:_______________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills Faults identified: Clutch cover:________________ Drive plate:_________________ Release bearing:___________________________ All nuts / bolts fitted:_______________________ Working area left clean and tidy:___________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Pop riveting task                                                                          Job number 17

| Pop riveting task Complete the Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor ‘s initials: | ( Communication/Numeracy skills) 100mm 50mm Join two pieces of metal plate; 100mm x 50mm with a lap joint using 3 x 3mm pop rivets or similar Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified: Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:______________________ Pop rivet gun:______________________ Measuring equipment:_______________________ Files/hacksaw/drill:____________________________________________ |  |
| Work results: self assessment for practical skills Are the three pop rivets equal distance apart:___________________________ Have all work piece edges been de-burred:______________________________ Working area cleaned and left tidy:___________________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Using a mutlimeter to test electrical and electronic components                                    Job number 18

| Using a multi-meter to test electrical/electronic components Complete the Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | (Communication/Numeracy skills) Test results of electrical and electronic components: Resistance of fuel petrol injector:____________________ Ohms Condition of fuse:____________________________________________________ Results of diode test:_________________________________________________ Results of twin filament bulb: 1. filament:____________ 2. filament:_____________ Resistance of plug lead:_________________________________________ Ohms Resistance of the resistor:________________________________________ Ohms Battery voltage:________________________________________________ Volts Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:___________________________ Was the environment effected by your work:_____________________ All tools returned and stored correctly:___________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills: Assortment of components: Petrol fuel injector Fuse Diode Twin filament bulb Plug lead Resistor Battery You will need access to the above components and a multi-meter, take readings and complete the test results. |  |
| Work results: self assessment for practical skills All components tested and results logged:_______________________________ All components returned and stored:____________________________________ Working area cleaned and left tidy:___________________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Remove and replace rack rod ends and check alignment 	                                Job number 19

| Remove and replace rack rod ends and check tracking Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:__________________ FWD/RWD:_____________________ Wheel nut torque:____________________ Nm Track rod end nut torque:_______ Nm Alignment/toe setting:_________ (mm or degrees): |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:__________________ Torque wrench:__________________ Tracking equipment:__________________ Ball joint splitter:__________________ | Questions to answer: (problem solving / improving own learning) How did you check the equipment before use:______________________________ State a symptom of excessive positive toe:______________________________ State a symptom of excessive negative toe:_______________________________ What causes tyre wear only in the tread centre:______________________________ Number of turns the track rod needed when fitted:___________________________ Faults identified:_______________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills All bolts and fittings correctly tightened with locking devices:_____________ Track rod ends fitted correctly:___________________________________ Tracking correct and checked:___________________________________ Wheels torque up and vehicle left clean:____________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Remove and replace exhaust silencer and check emission readings                                    Job number 20

| Remove and replace exhaust silencer and check emission readings Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle: __________________ Recommended CO:______ % HCC:_________ PPM Exhaust mounting bolts/clamp torque:_____________________________________ |
| --- | --- |
| Health & Safety and risk assessment Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:__________________ Torque wrench:__________________ Exhaust emissions tester:__________________ | Questions to answer: (problem solving / improving own learning) State a symptom of a hole in the exhaust:____________________________ What does the gas term CO mean:____________________ What does the gas term HCC mean:_____________________ What does the gas term CO2 mean:_____________________ What does the gas term 02 mean:_______________________ Fault identified:_______________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills All bolts and fittings correctly tightened with locking devices:_____________ Exhaust aligned and secure:______________________________________ Emissions: CO_______ % HC:_____________ PPM Vehicle left clean:____________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Remove and replace a cylinder head gasket using correct tightening procedures             Job number 21

| Remove and replace a cylinder head gasket using correct tightening procedures Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:__________________ Engine capacity:____________________ Inlet valve clearance:___________ mm Exhaust valve clearance:____________ mm Head tightening procedure: stage 1:______ stage 2:_______ stage 3:_____ |
| --- | --- |
| Practical skills Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:__________________ Torque wrench:__________________ Feeler blade:__________________ | Questions to answer: (problem solving / improving own learning) What is the correct tightening procedure for the cylinder head fixings:______________________________________________________________ State the method used to adjust the valves:___________________________ What material is the cylinder head made from:__________________________ What material is the cylinder block made from:_________________________ Faults identified:_______________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills All bolts and fittings correctly tightened with locking devices:_____________ Inlet valves adjusted:______________________________________ Exhaust valves adjusted:______________________________________ Covers and gasket tightened down:_________________________________ Vehicle left clean:____________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Remove and refit headlamp unit and check alignment                                      Job number 22

| Remove and refit headlamp unit and check alignment Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:__________________ Head lamp wattages for dip:________ Main beam:________ Side lamp:________ Indicator:_________ Brake lamp:______________ |
| --- | --- |
| Practical skills Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:_________________________________ Eye/ ear/ head protection needed (state):_______________________________ Other risks identified:_______________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:__________________ Torque wrench:__________________ Headlamp alignment equipment:__________________ | Questions to answer: (problem solving / improving own learning) State two checks to the headlamps before alignment is carried out:______________ Calculate the current flow in one 60w headlamp bulb:_________________________ (Use the formula W = V x A) Sketch the alignment pattern below: 0 0........................................................................................................................................0 0 Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly: ____________________________ Was the environment effected by your work:______________________ All tools returned and stored correctly:___________________________ |
| Work results: self assessment for practical skills All bolts and fittings correctly tightened with locking devices:_____________ Headlamp removed and fitted correctly:____________________________ Alignment correct and checked:__________________________________ Vehicle left clean:____________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Cam belt change on a CI (diesel) engine  	                                                                Job number 23

| Cam belt change on a CI (diesel) engine Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:_________________________ Engine capacity:___________ Recommended mileage change / time for the cam belt:_______________________ Crankshaft to camshaft ratio:____________________________________________ |
| --- | --- |
| Practical skills Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:__________________________ Eye/ ear/ head protection needed (state):________________________ Other risks identified:__________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:_______________________________________ Locking/marking devices:_______________________________ | Questions to answer: (problem solving / improving own learning) How many cylinders does the engine have:___________________________ Is the engine SOHC or DOHC:______________________________________ Did you use any locking devices and if so where:___________________________ Did the diesel pump need to be timed to the engine:____________________ State the importance of having the belt timed correctly:___________________ State the consequences of the belt being loose or breaking:______________________________________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:_______________________ All tools returned and stored correctly:____________________ |
| Work results: self assessment for practical skills Area left tidy and tools stored correctly:__________________________ Cam belt fitted and adjusted:_______________________________________ Timing marks all aligned and tensioned correctly:________________________ All nuts/bolts fitted and correctly tightened:___________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Remove and replace a suspension strut (Macpherson type). Remove and replace the spring 	Job number 24

| Remove and replace a suspension strut (Macpherson type) Remove and replace the spring Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:___________________________ Engine capacity:___________ Top mounting torque:_____________ Nm Lower mounting torque:_________ Nm |
| --- | --- |
| Practical skills Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:__________________________ Eye/ ear/ head protection needed (state):________________________ Other risks identified:__________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:_______________________________________ Suspension spring compressor:__________________________ Torque wrench:______________________________________ | Questions to answer: (problem solving / improving own learning) State three checks you made to the unit: 1.___________________________ 2.______________________________3.___________________________ What are the dangers when using spring compressors:_____________________________________________________________ Did you take the brake calliper off and how should it be supported: State a test for a damper:_________________________________________________________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:_______________________ All tools returned and stored correctly:____________________ |
| Work results: self assessment for practical skills Area left tidy and tools stored correctly:______________________ Spring and damper checked:____________________________________ Spring and damper reassembled:________________________________ All nuts/bolts fitted and correctly tightened:_________________________ Vehicle left clean and tidy:__________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Brake light switch removal, test and refit	             Job number 25

| Brake light switch removal, test and refit Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:___________________________ Brake bulb typical wattage:_______________________ w Position of brake switch:_________________________________________________ |
| --- | --- |
| Practical skills Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn:__________________________ Eye/ ear/ head protection needed (state):________________________ Other risks identified:__________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:_______________________________________ Multi-meter:________________________________________ | Questions to answer: (problem solving / improving own learning) Are any LEDs used in the braking lights (including high level type):_________________ What method of adjustment is available to the brake switch:_____________________ What is the resistance of the switch when operated:_______________________ Ohms Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:_______________________ All tools returned and stored correctly:____________________ Faults identified:__________________________ |
| Work results: self assessment for practical skills Area left tidy and tools stored correctly:__________________________ Brake switch removed and fitted:___________________________________ Brake lights work effectively:______________________________________ Vehicle left clean and tidy:__________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Using an engine fault code reader  	             Job number 26

| Using an engine fault code reader Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor’s initials: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:___________________________ Fault codes for: Coolant thermistor:________ Air mass meter:_________ Throttle position switch:__________ Lamda (02) sensor:_________ |
| --- | --- |
| Practical skills Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn: __________________________ Eye/ ear/ head protection needed (state):________________________ Other risks identified:__________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. Engine diagnostic equipment:___________________________________ State where it connects to:_____________________________________ | Questions to answer: (problem solving / improving own learning) What does the term OBD mean:___________________________________________ What does the term EOBD mean:__________________________________________ What does the term CAN mean in regards to CAN-BUS:___________________________ ____________________________________________________________________ You may have to search the internet or consult a text book for the above Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:_______________________ All tools returned and stored correctly:____________________ Faults identified:__________________________ |
| Work results: self assessment for practical skills Faults identified:____________________________ Fault code for Lambda sensor (02 sensor):_______ Fault code for air mass meter:__________________ Fault code for throttle position switch:____________ Fault code for Coolant thermistor:_______________ All codes cleared:___________________________ Vehicle left clean and tidy:__________________________ | Feedback from assessor Signature Date ____/_____/_______ |

Repair puncture in tyre                                                                            Job number 27

| Repair puncture in tyre Complete the vehicle details, Health & Safety, risk assessment, and tools/equipment before starting the practical skills of this job. This will need to be signed off first by your tutor. It is an important part of the skills requirements. Candidate’s name: Tutor initial: | Vehicle details and data (Communication/Numeracy skills) Make/Model of vehicle:___________________________ Tyre pressure:____________________ Speed rating:________________________ Diameter:________________________ Tyre sizes:___________________________ |
| --- | --- |
| Practical skills Identify Health & Safety and risks with this practical task Safety footwear, clothing always worn: __________________________ Eye/ ear/ head protection needed (state):________________________ Other risks identified:__________________________ Equipment used for practical skills You need to make sure all tools you use are checked before using, correctly used and returned in good condition after use. General tools:_______________________________________ Tyre drilling equipment:_______________________________ Tyre stones and dressing wheels:_______________________ Glues and rubber seals (mushrooms):____________________ | Questions to answer: (problem solving / improving own learning) What areas of a tyre should not be repaired:_____________________________________ Was an inner tube fitted:__________________________________________ Was the tyre a cross ply or radial ply:_________________________________________ What was the minimum tread depth on the tyre:______________________________________ What was the maximum tread depth of the tyre: _________________ Environmental issues: recycling, disposal of waste (ESDGC) Was there any waste recycled:____________________________ Was all waste disposed of correctly:____________________________ Was the environment effected by your work:_______________________ All tools returned and stored correctly:____________________ Faults identified:__________________________ |
| Work results: self assessment for practical skills Area left tidy and tools stored correctly:__________________________ Tyre repaired:___________________________________________________ Pressure checked:______________________________________________ Vehicle and area left clean and tidy:__________________________ | Feedback from assessor Signature Date ____/_____/_______ |

# Text boxes

Practical Training Workbook

3902 Entry level 3 and Level 1/                                              SCQF Level 3 and Level 4 in

Vehicle Systems Maintenance

Foundation Learning

Centre logo

Number plate

Measure your plate and enter dimensions in this box

Note: this is a replicated task and the number plate should be pre made to size from hard board. This task is basically a measuring and correct fitting exercise